## Slide 1: Baby monitor System
Code review

## Slide 2: System Overview
Extensible design allows customizing and future system extensions
PI-Server
Thermameter
RaspiMic
RaspiCam
Gui Client
Potential sensor
Potential Mobile Client
Data(Strings)
XML

## Slide 3
Temperature Sensor

## Slide 4
void Setup(void);
wiringpi.pinMode(25,1) #red light wiringpi.pinMode(24,1) #green light …
--------------------------------------------------------
void Led_con(int Temp);
wiringpi.digitalWrite(25,0) #red is on sleep(1)
wiringpi.digitalWrite(25,1) #red is off
…
--------------------------------------------------------
*Temp value is <40°C or <10°C .
void Led_con(int Temp);
wiringpi.digitalWrite(24,1) #green is on
…
--------------------------------------------------------
*Temp value is between 20°C and 27°C.
void cleanup(void);
wiringpi.digitalWrite(25,0) #red is off wiringpi.digitalWrite(24,0) #green is off
…
--------------------------------------------------------
1- Read Temp
2- Detects and reports the status of the system (etc. working normal, problems…)
Figure1.1: General view of the Temperature sensor’s functionality
First call
Last call
Initialize GPIO (sensor and LEDs)
Normal mode
Dangerous mode
Reset GPIO (sensor and leds)
Temperature Sensor

## Slide 5
Function Name | Argument | Test | Passed Information/ Action preformed | Expected result | Actual
readtempnow | Nothing | Temp sensor | Read from the sensor | Gives a temp reading within the room limit | Passed
geen | Int n | Green Led | 1 and 2 (on,off) | Green Led on then off | Passed
red | Int n | Red Led | 1 and 2 (on,off) | Red Led on then off | Passed
Led_con | Int Temp | Led+Temp | T=Max(40 °C) *Min(10°C) cab be used | Flashing the red led (Void) | Passed
Led_con | Int Temp | Led+Temp | T=NR* (x°C) Normal Range(20°C to 27°C) | Green led is on(Void) | Passed
setup | Nothing | Led+Temp | Nothing | Flashing the green led(Void) | Passed
cleanup | Nothing | Led+Temp | Nothing | Flashing both (green and red) (Void) | Passed
 |  | HTCase one | Touch the sensor with an ice cube ( in a plastic bag) | Temperature readings are decreasing | Passed
 |  | HTCase two | Place a hot object on the sensor | Temperature readings are increasing | Passed
Temperature Sensor

## Slide 6: (GUI) Client class Diagram
Model
View
Controller

## Slide 7: XML parsing and MVC:
Server sends XML messages to mainClient class ( blocked on read msg)
MainClient parses the received msg
Updates the appropriate model classes based on the xml tags
Model notifies the view of the changes
View gets updated accordingly

## Slide 8: jUnit Test cases:

## Slide 9
Jython Server

## Slide 11: Pyunit Testing

## Slide 13: Progress :
In progress

## Slide 14: Any Questions/Comments?

## Slide 15: Test results and implementation of RaspiMic
Function Name | Argument | Return type | Passed Information | Expected result | Actual result
Setup() | Nothing | variable for device just set up | Nothing | Nothing | Nothing
readData | variable for device just set up | Volume of maximum sample | Nothing | Nothing | Nothing
analyseData | Volume of maximum sample | Nothing | V=min(10000) | Send “1” to server | Send “1” to server
analyseData | Volume of maximum sample | Nothing | V=max(9999) | Send “0” to server | Send “0” to server

## Slide 16: Raspi Mic
readInput is a file in the Raspberry pi that reads the sound from the microphone and analyses the volume to verify if the sound is high or low and sends the result through TCP/IP to the server.
Snowball
Microphone
Raspi
Sound coming into microphone
readInput
USB

## Slide 17: Functionality of RaspiMic
Void analyseData(volume)
*volume <10000
Send “0” to server
Void setup()
Opens input device and
Sets its attributes for
reading data
Void readData(input device)
Read data and verify the max
Of the samples
Void analyseData(volume)
*volume >=10000
Send “1” to server
1, Read sound from
environment
2, Determine if sound is
dangerous or not
First step
Normal mode
Dangerous mode
Second step
Third step

## Slide 18: Image Stream top level System Diagram
Figure 2: Image Stream Top Level System Diagram [Raditya Budianto]

## Slide 19: Software Level System Diagram
Figure 3: Software Level System Diagram [Raditya Budianto]